## Slide 1: Inverse problems and imaging
Recap of last class
Inverse problems and DNA
Another inverse problem in medical imaging. Light attenuation model and the Radon transform
Working with images in Matlab

## Slide 2: Photograph 51, FT, double helix

## Slide 3: Medical imaging “Reconstruction” problems

## Slide 4: Medical imaging
Many medical images result from solving an inverse problem
Notes: PET, CT, MRI

## Slide 5: Enter patient: 65 year old man
Persistent dry cough
Mild fatigue
Smoked a pack a day for a decade
Lost 10 – 15 pounds in last six months

## Slide 6: Patient’s chest x-ray
Photo credit: Dr. Joseph Levine
Notes: - Concerning feature ~ 5cm
- Emphysema?

## Slide 7: Conventional x-rays
Roentgen (1895):
experiments with electron beams
1901: first physics Nobel

## Slide 8: First radiographs
Roentgen’s wife’s hand (1895)
Colleague’s hand (1896)
https://en.wikipedia.org/wiki/Wilhelm_Röntgen

## Slide 9: Electromagnetic spectrum
Material
(1/cm)
Attenuation

## Slide 10: Activity: model for attenuation?

## Slide 11: Attenuation: uniform material

## Slide 12: Attenuation: nonuniform material

## Slide 13: Attenuation: nonuniform material
. . .

## Slide 14: Attenuation: nonuniform material
. . .
. . .
. . .

## Slide 15: Attenuation: nonuniform material
. . .
Riemann Sum

## Slide 16: Attenuation: nonuniform material
. . .

## Slide 17: What is known?
known input x-ray intensity
measureable output x-ray intensity
x-ray projection
Notes: The map of mu(x) into its’ line integrals the radon transform of mu(x)

## Slide 18: What is known? What is unknown?
KNOWN!
UNKNOWN!
Inverse problem, image reconstruction problem
Given:
Find:

## Slide 19: X-rays: Shadows

## Slide 20: Tomography: solve for
Tomography: “Any of several techniques for making detailed x-rays of a
predetermined plane section of a solid object while blurring out the images
of other planes.”
1 cm carcinoma
pulmonary embolism
Chest Computed Tomography (CT) Images

## Slide 21: Patient’s CT Scan
Photo credit: Dr. Joseph Levine
Notes: Red arrow to the clearly visible mass, as well as what other objects are
Notice in this case – one cross section is enough for now, but….
- Mass 7cm across
- Enlarged lymph nodes

## Slide 22: Basic idea: view 1
Semi-opaque cylinder with 5 smaller cylinders embedded
Top view
light

## Slide 23: Basic idea: view 2
Semi-opaque cylinder with 5 smaller cylinders embedded
light
Top view

## Slide 24: CT systems
x-ray source
detector
parallel beam
fan beam
detector
x-ray source
Notes: So how do we get these great CT images? CT scanners measure I, the x-ray intensity after attenuation through the patient. For some small block of width delta x with constant attenuation f, the x-ray intensity leaving the object can be determined by solving dI/dx = -f I with initial condition being the initial intensity of the x-ray beam. Building this up for many small blocks with width delta x and different constant attenuations, and in the limit as delta x goes to zero, we can write blah. Taking the log of both sides and defining g = …, we have the following integral equation. G here is called the measured projection, which is given, since we know the initial input intensity and the measured intensity from the scanner. So the goal is, given these measured projections g, can we determine the patient’s attenuation function f. Or, solve an integral equation.
Now we have the model for one x-ray. But for a CT scan, we use many x-rays. The simplest configuration is to have an x-ray source on a line and a detector directly across from it, with the x-ray beams running parallel to each other. Then after the x-rays hit the detector, we rotate the entire configuration, and do it all again. This was the first type of scanner built in the 70s; no one uses this anymore. A more complicated version is the one shown here, called fan-beam because the x-ray source emanates from a point in a fan. The detector is curved.

## Slide 25: Modern CT system
Helical configuration

## Slide 26: Break

## Slide 27: What is an image?
An image is a matrix
A pixel vi,j is a value in a matrix
For a simple greyscale image, black=0, white=1, and numbers in-between represent greys
5
1
2
3
4
1
2
3
4
v4,4 = 0
v5,1 = 1
v2,5 = 0.5
5
row
column

## Slide 28: Matlab: simple image
clear all;
close all;
N = 5;
V = eye(N);
%identity matrix:
%1 = white, 0 = black
imshow(V, 'InitialMagnification', 'fit');
colorbar
%change element (2,5) to gray
V(2,5) = .5;
imshow(V, 'InitialMagnification', 'fit');
colorbar('southoutside', 'Fontsize', 15);

## Slide 29: Matlab: simple image
row
column

## Slide 30: Real images
http://www.telegraph.co.uk/news/newstopics/howaboutthat/11963318/Uber-delivers-cute-kittens-to-stressed-workers-on-National-Cat-Day.html

## Slide 31: Kitten in Matlab
Kitten is a 387 by 620 by 3 matrix (the third dimension is for color)
How big is the image? Type whos.

## Slide 32: Kitten in Matlab
Black and white kitten is 387 x 620

## Slide 33: Partial information: shadows

## Slide 34: Radon transform
1
1
0
0
0
0
1
1
rows
columns

## Slide 35: Radon transform
0
1
1
0
0
0
1
1
row i

## Slide 36: Shadows: Radon transform
Radon Transform

## Slide 37: Radon transform
Radon Transform R
Image

## Slide 38: Second view: Radon transform

## Slide 39: Second view
Image
Radon Transform R

## Slide 40: Lab next Tuesday
Images and Radon transform in Matlab
Bring your computer!